## Slide 1
Path-Conditioned Next-Best-View Planning for
Cooperative Aerial-Ground Mars Scouting
on a 3D Gaussian Splatting Substrate
Jatin Satyam | SES 598 Space Robotics and AI
School of Manufacturing Systems and Networks · Arizona State University

## Slide 2
Motivation
2 / 12
The problem with Ingenuity
Perseverance moves meters per sol. Each traverse requires hours of human-in-the-loop planning. Ingenuity flew on commanded waypoints — not as an autonomous teammate.
The natural question
When the drone is given agency: how should it pick its next viewpoint, what should it be looking for, and how should that decision be informed by the rover's plan?
Three converging lines of work
① Active 3DGS: per-Gaussian uncertainty as a usable view-selection signal (ActiveGS, FisherRF, RT-GuIDE)
② Cooperative aerial-ground IPP: path-conditioning as the standard coupling mechanism (Traversing Mars, Seeker-Supporter)
③ Planetary traversability: uncertainty-aware rover planning (LSRC field-deployed at NASA Ames + White Sands, 2026)
This work sits at the intersection of all three lines.

## Slide 3
Problem Statement
3 / 12
Cooperative aerial-ground scouting on Mars-analog terrain
A drone surveys terrain ahead of a rover, building a 3DGS representation. The rover consumes a traversability costmap derived from the splat field. Cells with high per-Gaussian reconstruction uncertainty → high traversability uncertainty → rover prefers to avoid or request re-survey.
The view-selection objective
Which candidate viewpoint maximises expected reduction in traversability uncertainty along the rover's planned path?
v* = argmax u(v) = Σ P(c ∈ r) · Δσ²_c(v)
Cross-agent: the path r belongs to the rover, not the drone selecting the view.

## Slide 4
Related Work — Four Clusters, One Gap
4 / 12
Active 3DGS NBV
ActiveGS (RA-L 2025)
FisherRF (ECCV 2024)
AG-SLAM, RT-GuIDE
Per-Gaussian uncertainty methods
Gap: UAV outdoor demos; coverage-driven gain; no traversability semantics
Cross-Agent 3DGS
RaEM (arXiv 2024)
Khass et al. (Oct 2025)
Gap: Indoor, collision-risk; discrete-waypoint masking; single-agent path, not rover's path
Cooperative Mars IPP
Traversing Mars (RA-L 2025)
Seeker-Supporter cluster
Gap: Follower-path-aware utility; occupancy/GP map substrate, not 3DGS
Planetary Traversability
Endo et al. (RA-L 2024)
LSRC (Feb 2026, real hardware)
Gap: Uncertainty-aware rover planning; no 3DGS, no aerial visual scout, no active NBV
Each cluster closes one piece. The specific combination — 3DGS + aerial scout + traversability + Mars-analog — remains open in the surveyed literature.

## Slide 5
The Contribution: A Targeted Specialisation
5 / 12
What this work is
Applying recently published methods to a substrate + sensing modality + task semantics combination not yet covered in the surveyed literature.
3DGS Substrate
RaEM + Khass apply this
New: with traversability semantics
Aerial Visual Scout
Traversing Mars does this
New: on a 3DGS map, with active NBV
Traversability Semantics
LSRC does this on real hardware
New: per-Gaussian uncertainty routed in
Mars-Analog Setting
HiRISE DTM of Jezero Crater
Established methodology (MARTIAN, Bland)
Each ingredient is precedented. The recipe — as far as we can tell — is not.

## Slide 6
System Design (Full Architecture)
6 / 12
Drone Survey & Control
X500 quadrotor · MulticopterVelocityControl · adaptive survey pattern driven by NBV planner
Online 3DGS Front-End
MonoGS or DUSt3R/MASt3R · pilot uses offline COLMAP + splatfacto as stand-in
Per-Gaussian Uncertainty
Predictive Photometric Uncertainty (plug-and-play) · pilot uses opacity + scale proxy
Path-Conditioned NBV
Gain function (Sec. V) · inputs: 3DGS field + rover path + candidate viewpoints
Traversability Projection
Per-Gaussian uncertainty → 2.5D height-map grid · bridge from splat domain to rover costmap
Uncertainty-Aware Rover
A*/D* with per-cell uncertainty as soft cost · wait-for-more-info when path is uncertain
Drone → 3DGS → Uncertainty → Gain → NBV → Rover
Pilot experiment exercises the Gain function + Per-Gaussian Uncertainty layers. Remaining components are described and treated as future work.

## Slide 7
Path-Conditioned Gain Function
7 / 12
Soft path-likelihood prior
P(c ∈ r) = exp( −d(c,r)² / 2τ² )
d(c,r) = perpendicular distance from cell c to rover trajectory r
τ = corridor width ≈ rover safety envelope + replanning slack
Path-conditioned gain
u(v) = Σ_c P(c ∈ r) · Δσ²_c(v)
Δσ²_c(v) = expected uncertainty reduction if drone observes from v
Drone selects v* = argmax_v u(v)
RaEM (special case)
P(c) = 𝟙[min_k ‖c−w_k‖ < R]
Hard sphere around each waypoint
→ our Eq. (2) recovers this with degenerate τ→0
Khass (related)
Weight per-Gaussian along same agent's path using Fisher information
Our work: cell domain, rover's path, traversability semantics
Our generalisation
Soft corridor prior
Cross-agent: rover path → drone gain
Traversability uncertainty, not Fisher info
GP-UCB extension: u_UCB(v) = Σ_c P(c ∈ r)·[μ_c(v) + β^½·σ_c(v)] — future work.

## Slide 8
Pilot Experiment — Setup
8 / 12
Terrain
HiRISE Digital Terrain Model · Jezero Crater
(same source as JPL Perseverance operations pipeline)
40 m patch · 1 m/pixel resolution
MOLA+HiRISE fused DTM · 513×513 heightmap
Blender-rendered Gazebo world with:
· Mars-analog rock obstacles
· Mars solar irradiance lighting
· DARTSim physics backend
Reconstruction pipeline
COLMAP sparse SfM → Nerfstudio splatfacto trainer
~14,000 Gaussians covering the area of interest
Pilot scope
① Per-Gaussian uncertainty visualisation
② Path-conditioned vs uniform viewpoint gain
Offline counterpart of online front-end — deliberately scoped
14k
Gaussians reconstructed
10
Survey waypoints
(8m AGL)
50×50
Grid resolution
for gain eval
10
Candidate
viewpoints

## Slide 9
Pilot Result 1 — Per-Gaussian Uncertainty
9 / 12
Uncertainty proxy
Combined opacity-based + covariance-volume proxy
Low opacity → high uncertainty
Large scale → under-constrained
What the figure shows
Dense core (center-right) = certain
Sparse periphery (edges, turn-arounds) = uncertain
Pattern directly reflects survey coverage geometry
Upgrade path
Predictive Photometric Uncertainty is plug-and-play — post-hoc, no retraining

## Slide 10
Pilot Result 2 — Path-Conditioned vs Uniform Gain
10 / 12
VP09
Path-conditioned
selects → (-1.5, 2.0)
VP04
Uniform baseline
selects → (0, 2.0)
DIFFER
Selection differs = TRUE
Path-conditioning is not a reparameterisation

## Slide 11
Simulation Environment & Demonstration
11 / 12
Mission start: X500 drone +
Mars rover on Jezero terrain
ALL SYSTEMS RUNNING:
Drone SURVEY · Rover NAVIGATING · TRN active
Mission complete:
WP 18/18 · 0.73m from dome center
Path to real deployment via PX4 Autopilot
Drone control layer uses uXRCE-DDS — identical bridge used in PX4 production hardware stack.
Replacing SITL with Pixhawk 6C preserves same DDS namespace + mission_config.yaml.
Offboard mode arming + 10 Hz TrajectorySetpoint sequence is identical between SITL and hardware.

## Slide 12
Conclusion
12 / 12
What was demonstrated
A path-conditioned gain function that generalises RaEM's discrete-waypoint masking to a soft path-likelihood prior, applied to a HiRISE-derived 3DGS reconstruction of Jezero Crater. Path-conditioning shifts the selected viewpoint relative to a uniform-weight baseline — the pilot shows the specialisation is grounded in something concrete.
Honest scope
· Sim-only — no real hardware (LSRC, ActiveGS, Traversing Mars all have real demos)
· Offline 3DGS pipeline — online front-end not implemented
· Single fixed rover trajectory — probabilistic plans not exercised
· Per-Gaussian proxy is weak — calibrated UE is plug-and-play upgrade
Future work
· Stream MonoGS / MASt3R front-end on RTX 4060
· Upgrade to Predictive Photometric Uncertainty
· Wrap NBV planner in ROS2 node + integrate with flight loop
· Crazyflie / Tello + TurtleBot tabletop real-hardware demo
· Multi-drone extension
35%
Confidence cap —
honest specialisation
29
References
cited
7pp
IEEE-format
report
TRUE
Selection
differs
Each ingredient is precedented. The recipe, as far as we can tell, is not.